## Slide 1: Trebuchet STEM Physics
Fortuna High School:
Errin Odell, Sara Dixon, Kim Peterson, Rob Marshall

## Slide 2: Tutorials
How to use Tracker video tutorial
How to analyze counterweight Tracker video tutorial
How to analyze kinetic energy tracker video tutorial

## Slide 3: Tools and Materials Image Link
Tools
  Cross cut saw
  Square (carpenters and quick)
  Screw driver
  Drill
  Hand saw
  Caliper
  Pliers
  Hammer
  Meter stick
  Hole saw (large drill bits)
  Drill bits
  Leather cutting scissors
  Chisel
  Sand paper
  Glue gun (lots of glue)
  Tin Snips
  Hack Saw
  Tripod
  Cell phone tripod mount
  Camera
  Computer
  Tracker Software
Materials
  Glue
  Wood (I rip 2 X 4 into ¾”X ¾”) pieces
  Nylon String (Used for cement forms)
  Zip Ties (various sizes)
  Skateboard wheels
  Skateboard Wheel bearings (axle and wheels)
  Axle (diameter)
  Door skins (I cut this up for gussets)
  Electrical tape
  Round sheet rock corners
  Metal plumbers tape
  Various eye hooks
  Nuts and Bolt for skateboard wheels
  Various washers
  Denim
  Leather
  Old Bike wheel spokes (end of trebuchet arm)
  Bouncy ball (amazon)

## Slide 4: Internet and Movie Research
NOVA Secrets of Lost Empires Medieval Siege
  Movie Link
  Movie Questions Link: Some of the links in the questions sheet are outdated but you can search for the answers.
Internet Research
  Internet Research Links
  Trebuchet Sketch Handout Link
    Have them take notes using the research links. Then have students make their Trebuchet sketch based on the handout.
  Sample Trebuchet Sketch Link

## Slide 5: Design
Using the Trebuchet Sketch from the research they now create a full scale drawing to be used for the construction phase.
Full scale drawing (I suggest they use 45 degree angles on the frame to simplify construction cuts).
  Design Handout Link
  Example work Links
    With Materials
    Without Materials

## Slide 6: Trebuchet Construction and Engineering Design Outline
Construction begins with the sides and base from the scale drawing, then the Design Engineering Process Activities begin.
From the scale drawing and design constraints
    Sides from scale drawing
    Base from scale drawing
    Arm from the design constraint
    Counterweight: 1kg from the design constraint
Design Engineering Process Activities
    Trigger: this is a safety issue…constraints.
    Counterweight Attachment
    Trough: Movable so the Trebuchet can adjust its aim
    Sling: Sling length will affect the release point
    Pouch: A good pouch will release the ball consistently AFTER the sling releases
    Counterweight Mass Efficiency: More mass is not necessarily more efficient. It suffers from the law of diminishing returns

## Slide 7: Engineering Design Process Safety Trigger
Without a working trigger the trebuchet is a safety issue.
Trigger Design Constraints Handout Link

## Slide 8: Engineering Design Process Counterweight Attachment
The students refer back to their research to determine the best counter weight attachment and whether to put wheels on it or not. The video had two examples of Trebuchets. One with wheels and one with a swinging counter weight attachment. They are constrained to 1kg of mass for the counterweight. Each combination is video taped and analyzed in Tracker software. The final decision is made by analyzing the path of the counterweight and the velocity of the throwing arm.
Counterweight Attachment Methods
  Fixed Counterweight, No wheels
  Fixed Counterweight, Wheels
  Swinging Counterweight, Wheels
  Swinging Counterweight, No Wheels
Trebuchet Counterweight Analysis Handout
Trebuchet Tracker Analysis Tutorial

## Slide 9: Engineering Design Process and Physics Sling Length and Transfer of Energy from Potential to Kinetic
Students must have a video of their Trebuchet firing with a 50cm sling. Do not use a pouch at this point. Fix a bouncy ball on the end of the sling. The goal of this lesson is to make sure all the potential energy is released from the counter weight at the exact moment the sling is released from the throwing arm. Start with a class discussion of the engineer design process. Second have a think-ink-pair share with the trebuchet sling release diagrams. Last have them look at a video of their trebuchet firing with a 50cm sling and fill out the Trebuchet Redesign Template.
Handouts
  Engineering design process template
  Trebuchet sling release diagrams
  Trebuchet Redesign Template Handout

## Slide 10: Engineering Design Process: Pouch Design
Now they need to make a pouch which releases consistently.
Use the internet to research potential pouch designs.
Create templates out of paper.
Use the paper templates to make a denim prototypes.
Test the prototypes with video analysis.
Taking videos and analyzing them helps determine if the pouch opens ad releases the ball when the sling releases from the throwing arm.
Make the final design out of leather.

## Slide 11: Good Pouch Release Videos
Good Sling Release Videos. Notice the pouch releases after the sling releases.
  Video 1
  Video 2

## Slide 12: Finding the Most Efficient Mass Engineering Design Process Physics - Transfer of Energy Efficiency
This is the physics part of the lesson. Students change the mass of the counterweight, calculate the change in potential energy, take a video of the projectile, determine the kinetic energy of the projectile, then determine the efficiency of the trebuchet. The goal is to make the most efficient trebuchet. They will find that adding mass will make the projectile go further but make the efficiency suffer.
Handouts
  Potential Energy to Kinetic Energy Worksheet Link
Tutorial
  How to analyze kinetic energy with Tracker

## Slide 13: Engineering Process Precision and Accuracy
Accuracy is defined as the closeness of a measured value to a standard or known value.
Precision is defined as the closeness of two or more measurements to each other.
The final goal is to tune the trebuchet so they can hit a wooden block wall (accuracy) and hit it consistently (precision).